## Slide 1: Module 1: Internetworking
Lesson 1: Networking Overview

## Slide 2: Internetworking Module
Module Description: ​
The intent of this Knowledge Unit is to provide students with an understanding of networking and internet protocols.
Topics:​
  Lesson 1: Networking Overview​
  Lesson 2: Internetworking
  Lesson 3: PCAP File Format

## Slide 3: Learning Outcomes
Upon completion of this lesson:
  Students will be able to describe and discuss data network architectures and protocols.
  Students will be able to describe the ISO networking model.

## Slide 4: Background
What are networked systems?
  A set of devices (hosts) connected by a communication medium that are able to share data through transmission over the media
  System Characteristics include (but are not limited to)
    Physical properties of the communication signals
    Physical topology of the communication medium and logical topology of the data transmission
    Format and timing of the signals
    Error and Flow control, connection management, recovery, security

## Slide 5: Background
Why do we use networked systems?
  To facilitate the sharing of resources
    Printers
    Disk/Tape drives
    Computational Power
    Data Sets
  To permit the distribution of workload
    Concurrent/parallel computing
    Client-server computing
    Fault tolerance
  To facilitate the transfer of information
    Database transactions
    Electronic mail
    Networked distribution of data -- archives

## Slide 6: Background
How do data networks work?
  Systems communicate over a shared communication medium according to an agreed upon convention (standard).
  Several sets of standards currently exist:
    DoD: TCP/IP
    ISO: OSI model
    Commercial: SNA, IPX, X.25, ...
    Proprietary
  In this course we will basically follow the seven layer approach defined by ISO with additional emphasis on the DoD hierarchy.

## Slide 7: Background
DOD Model
  hierarchical arrangement of entities that may communicate with peer entities in another system
  one entity within a system provides services to other entities, and also uses the services of other entities
  places importance on internetworking, i.e., when two communicating entities are not attached to the same network
  places equal importance on connectionless and connection oriented systems
  consists of 802.X, X.25, TCP/UDP/IP and FTP, TELNET, SMTP, NSP and SNMP protocols

## Slide 8: Background
ISO/OSI Model
  communication functions are partitioned into a vertical set of seven layers
  each layer performs a related subset of functions required for communication
  each layer provides services to the next highest layer while depending on the next lower layer to perform more primitive functions
  decomposes one problem into a number of more manageable subproblems
  communication is achieved by having corresponding (peer) entities in the same layer in two different systems communicate via a protocol

## Slide 9: Background
  each protocol entity sends data down to the next lower layer in order to get the data across to its peer entity
  each entity communicates with entities in the layers above it and below it, across an interface
  analogous to structures programming
  protocols include: 8802.X, 8072/3, 8236/7, 8822/3/4/5, ...

## Slide 10: Background
ISO/OSI Reference Model
  Provides a common basis for coordination of standards.
  Based on a hierarchical model
    Application Layer
    Presentation Layer
    Session Layer
    Transport Layer
    Network Layer
    Data Link Layer
    Physical Layer

## Slide 11: Background
Application
Presentation
Session
Transport
Application
Presentation
Session
Transport
Network
Data Link
Physical
Application
Presentation
Network
Data Link
Physical
Network
Data Link
Physical
Network
Data Link
Physical
Network
Data Link
Physical
Network
Data Link
Physical
Network
Data Link
Physical

## Slide 12: Background
Layers of the ISO/OSI Hierarchy
  Physical Layer
    This layer is responsible for defining the method of transmitting bits of information across a transmission medium. This layer includes mechanical electrical, functional and procedural specifications. Examples of such standards are EIA-232-D (RS-232), Ethernet, Modem Standards.
  Data Link Layer
    This layer is responsible for managing transmission of information across a single communication link. It attempts to add reliability, flow and error control, and communication management (HDLC, LAP-B)

## Slide 13: Background
  Network Layer
    This layer is responsible for providing communication between two hosts across a communication network. It provides the interface such that higher layers need not know about the underlying topology. It provides connection management, routing, and error and flow control. (X.25 is best known protocol, DoD’s IP fits in here too).
  Transport Layer
    Provides reliable end-to-end communication between processes on hosts. Ensures error-free delivery and sequencing and provides connection management. (DoD’s TCP best known).

## Slide 14: Background
  Session Layer
    Provides ability to control flow of information (the dialogue) between end users, grouping of data and checkpointing for error-recovery.
  Presentation Layer
    This layer manages the syntax of the data being transmitted. It is responsible for conversion between different formats and representations. (e.g., virtual terminals, cryptography)
  Application Layer
    This layer provides management functions to support distributed applications utilizing the OSI environment.

## Slide 15: Background
DOD (TCP/IP) Network Stack
Application Layer | SMTP, HTTP, FTP, etc.
Transport Layer | TCP, UDP
Network Layer | IP. ICMP, IGMP
Logical Link Layer | Device Drivers (IEEE802.x)
Physical Layer | Network Adapters