## Slide 1: Model 6 Introduction to Network Security
Lesson 2: Network encryption and protocols

## Slide 2: Module 6: Introduction to Network Security
Module Description:
This module introduces network security. In the first micro module, students will be given an overview of networks, and then move to network attacks, such as Denial-of-service attacks. The second micro module discusses network encryption and some network protocols, such as IPV6, SSH, SSL/TLS, HTTPS, IPSec. Network defense techniques are introduced in the third micro module. This micro module focuses on techniques such as firewalls, intrusion detection and prevention systems, honeypot.
Topics:
  Lesson 1: Network basics and threats
  Lesson 2: Network encryption and protocols
  Lesson 3: Network defense technologies

## Slide 3: Lesson 2: Network encryption and protocols
Topics:
  Network encryption concepts and tools
  Network protocols (IPv4, IPv6, SSH, SSL/TLS, IPSec, HTTPS)
Learning Outcomes:
  Upon completion of this lesson:
  Students will be able to understand some of the network protocols which have security features built in (such as SSH, SSL/TLS, HTTPS, IPSec).
  Students will be able to describe network data encryption.

## Slide 4: Warm up
How does data transfer from software/application, over the network, to the user at the other end?
How to protect the data while its transferring over the network?

## Slide 5: Encryption for network
Link Encryption
  Data are encrypted right before the transfer over the physical communications link and are decrypted when they arrive at the destination system.
  Encryption occurs at layer 1 or layer 2 in the OSI model.
  Link encryption protects the message in transit between two computers, but the message is in plaintext inside the hosts.

## Slide 6: Encryption for network (cont.)
End-to-End Encryption
  End-to-end encryption provides security from one end of a transmission to the other.
  The encryption is performed at the highest levels (usually at level 7, sometimes at level 5 or level 6 of the OSI model).
  The encryption can be done by software running on the host computer.
  Decryption will be done by the software on the other end.

## Slide 7: Link Encryption vs. End-to-End Encryption
Link encryption:
  faster
  easier for the user
  uses fewer keys
End-to-end encryption:
  more flexible
  can be used selectively
  done at the user level
  can be integrated with the application

## Slide 8: Browser Encryption
Browsers can encrypt data for protection during transmission.
The browser and the server negotiate a common encryption key, so even if an attacker does hijack a session at the TCP or IP protocol level, the attacker cannot exchange data because of not having the proper key.
SSH encryption
SSL and TLS encryption

## Slide 9: Secure Shell (SSH)
Originally developed for UNIX but now available on most Oss.
SSH provides an authenticated, encrypted path to the shell over the network.
The SSH protocol involves negotiation between local and remote sites to agree on encryption algorithm and authentication.
SSH protects against spoofing attacks and modification of data in communication.

## Slide 10: SSL and TLS
Secure Sockets Layer (SSL) was designed in the 1990s to protect communication between a web browser and server.
Three versions: SSL 1.0 (private), SSL 2.0 (1995), SSL 3.0 (1996)
In 1999, it was renamed to Transport Layer Security (TLS).
TLS is designed use TCP to provide a reliable end-to-end secure service.
SSL is implemented layer 4 (transport) of the OSI model.

## Slide 11: HTTPS (HTTP over SSL)
HTTPS - Combination of HTTP (HyperText Transfer Protocol) and SSL to implement secure communication between a web browser and a web server.
Built into all modern Web browsers
URL addresses begin with https://
Agent acting as the HTTP client also acts as the TLS client. Closure of an HTTPS connection requires that TLS close the connection with the peer TLS entity on the remote side, which will involve closing the underlying TCP connection.
A normal HTTP connection uses port 80. If HTTPS is specified, port 443 is used, which invokes SSL.

## Slide 12: Onion Routing
Both link encryption and end-to-end encryption, the transferred data was secured by encryption. However, the addressing data were exposed.
Onion routing prevents an eavesdropper from learning source, destination, or content of data in transit in a network.
  The intermediate host that sends the message to the final destination cannot determine the original sender, and
  The host that received the message from the original sender cannot determine the ultimate destination

## Slide 13: Onion Routing example
Example:
  To send untraceable data from host A to host B, A picks some number of forwarding hosts, call them X, Y, and Z.
  Host A first encrypts the communication using B’s public key. A then appends a header from Z to B, and encrypts the result with Z’s public key. A then puts a header on that from Y to Z and encrypts that under Y’s public key. A then puts a header on that communication from X to Y and encrypts that under X’s public key. Finally, A puts on a header to send the package to X.

## Slide 14: IP version 4
32-bit (4-byte) addressing
  The total number of IPv4 addresses is 4 294 967 296
The text form of the IPv4 address is nnn.nnn.nnn.nnn, where 0<nnn<255 and each n is a decimal digit.
IP header: variable length of 20-60 bytes, depending on IP options present.

## Slide 15: IP version 6
128 bits long (16 bytes) addressing
The text form of the IPv6 address is xxxx:xxxx:xxxx:xxxx:xxxx:xxxx:xxxx:xxxx, where each x is a hexadecimal digit, representing 4 bits.
IP header: Fixed length of 40 bytes.

## Slide 16: IPSec
As a part of the IPv6 suite, the IETF (Internet Engineering Task Force) adopted IPSec, or the IP Security Protocol Suite.
IPSec was designed to address some drawbacks of IPv4, such as being subject to spoofing, eavesdropping, and session hijacking.
IPSec is implemented at the IP layer, so it affects all layers above it, in particular TCP and UDP. And it does not require any change to the existing TCP and UDP protocols.

## Slide 17: Goals of IPSec
Prevent from IP spoofing
  A critical weakness of IPv4 is that there is no authentication of the source IP addresses. Therefore the IP address can be spoofed.
Protect integrity and/or confidentiality of packets
Prevent replay attack.
  Relay attack - An attack that involves the capture of transmitted authentication or access control information and its subsequent retransmission with the intent of producing an unauthorized effect or gaining unauthorized access.
Provide security for upper layer protocols and applicaitons

## Slide 18: IPSec modes
There are two operation modes in IPSec: transport mode and tunnel mode.
In transport mode, security protection is provided to traffic from one host to another (end-to-end).
In tunnel mode, security protection is provided to traffic from one gateway of a network to the gateway of another network (virtual private network, VPN).

## Slide 19: Virtual Private Network
A virtual network, built on top of existing physical networks, that provides a secure communications tunnel for data and other information transmitted between networks.
VPN reduces the overall telecommunication infrastructure, and the cost of management, maintenance of equipment.

## Slide 20: Summary
Topics:
  Network encryption concepts and tools
  Network protocols
    IPv4
    IPv6
    SSH
    SSL/TLS
    IPSec
    HTTPS

## Slide 21
Please attribute Dr. Jim Alves-Foss and Dr. Jia Song, University of Idaho
Except where otherwise noted, this work is licensed under https://creativecommons.org/licenses/by-nc-sa/4.0/ Not withstanding the non-commercial license terms, non-profit educational institutions are granted a non-exclusive license to adapt and use this material, with attribution. Creative Commons and the double C in a circle are registered trademarks of Creative commons in the United States and other countries. Third party marks and brands are the property of their respective holders.
Project sponsored by the National Security Agency under grant Number H98230-17-1-0199. The United States Government is authorized to reproduce and distribute reprints notwithstanding any copyright notation herein.