## Slide 1: Module 0: Introduction
Lesson: Networking Overview

## Slide 2: Networking Background (part 1)
What are networked systems?
  A set of devices (hosts) connected by a communication medium that are able to share data through transmission over the media
  System Characteristics include (but are not limited to)
    Physical properties of the communication signals
    Physical topology of the communication medium and logical topology of the data transmission
    Format and timing of the signals
    Error and Flow control, connection management, recovery, security

## Slide 3: Networking Background (part 2)
Why do we use networked systems?
  To facilitate the sharing of resources
    Printers
    Disk/Tape drives
    Computational Power
    Data Sets
  To permit the distribution of workload
    Concurrent/parallel computing
    Client-server computing
    Fault tolerance
  To facilitate the transfer of information
    Database transactions
    Electronic mail
    Networked distribution of data -- archives

## Slide 4: Networking Background (part 3)
How do data networks work?
  Systems communicate over a shared communication medium according to an agreed upon convention (standard).
  Several sets of standards currently exist:
    DoD: TCP/IP
    ISO: OSI model
    Commercial: SNA, IPX, X.25, ...
    Proprietary
  In this course we will basically follow the seven layer approach defined by ISO with additional emphasis on the DoD hierarchy.

## Slide 5: Networking Background (part 4)
DOD Model
  hierarchical arrangement of entities that may communicate with peer entities in another system
  one entity within a system provides services to other entities, and also uses the services of other entities
  places importance on internetworking, i.e., when two communicating entities are not attached to the same network
  places equal importance on connectionless and connection oriented systems
  consists of 802.X, X.25, TCP/UDP/IP and FTP, TELNET, SMTP, NSP and SNMP protocols

## Slide 6: Networking Background (part 5)
ISO/OSI Model
  communication functions are partitioned into a vertical set of seven layers
  each layer performs a related subset of functions required for communication
  each layer provides services to the next highest layer while depending on the next lower layer to perform more primitive functions
  decomposes one problem into a number of more manageable subproblems
  communication is achieved by having corresponding (peer) entities in the same layer in two different systems communicate via a protocol

## Slide 7: Networking Background
  each protocol entity sends data down to the next lower layer in order to get the data across to its peer entity
  each entity communicates with entities in the layers above it and below it, across an interface
  analogous to structures programming
  protocols include: 8802.X, 8072/3, 8236/7, 8822/3/4/5, ...

## Slide 8: ISO Model
ISO/OSI Reference Model
  Provides a common basis for coordination of standards.
  Based on a hierarchical model
    Application Layer
    Presentation Layer
    Session Layer
    Transport Layer
    Network Layer
    Data Link Layer
    Physical Layer

## Slide 9: ISO Model (part 1)
Application
Presentation
Session
Transport
Application
Presentation
Session
Transport
Network
Data Link
Physical
Application
Presentation
Network
Data Link
Physical
Network
Data Link
Physical
Network
Data Link
Physical
Network
Data Link
Physical
Network
Data Link
Physical
Network
Data Link
Physical

## Slide 10: ISO Model (part 2)
Layers of the ISO/OSI Hierarchy
  Physical Layer
    This layer is responsible for defining the method of transmitting bits of information across a transmission medium. This layer includes mechanical electrical, functional and procedural specifications. Examples of such standards are EIA-232-D (RS-232), Ethernet, Modem Standards.
  Data Link Layer
    This layer is responsible for managing transmission of information across a single communication link. It attempts to add reliability, flow and error control, and communication management (HDLC, LAP-B)

## Slide 11: ISO Model (part 3)
  Network Layer
    This layer is responsible for providing communication between two hosts across a communication network. It provides the interface such that higher layers need not know about the underlying topology. It provides connection management, routing, and error and flow control. (X.25 is best known protocol, DoD’s IP fits in here too).
  Transport Layer
    Provides reliable end-to-end communication between processes on hosts. Ensures error-free delivery and sequencing and provides connection management. (DoD’s TCP best known).

## Slide 12: ISO Model (part 4)
  Session Layer
    Provides ability to control flow of information (the dialogue) between end users, grouping of data and checkpointing for error-recovery.
  Presentation Layer
    This layer manages the syntax of the data being transmitted. It is responsible for conversion between different formats and representations. (e.g., virtual terminals, cryptography)
  Application Layer
    This layer provides management functions to support distributed applications utilizing the OSI environment.

## Slide 13: DoD Model
DOD (TCP/IP) Network Stack
  Developed in the 1970s
  Part of project that grew into the modern internet
DoD Layers | ISO Layers | Protocols
Process Layer | Application Layer | SMTP, HTTP, FTP, etc.
Host-to-host Layer | Transport Layer | TCP, UDP
Internet Layer | Network Layer | IP. ICMP, IGMP
Network Access Layer | Logical Link Layer | Device Drivers (IEEE802.x)
 | Physical Layer | Network Adapters

## Slide 14: Encapsulation
For any layered network model, encapsulation is key. For example, for an http request:
HTTP
HTTP
TCP Header
HTTP
TCP Header
IP Header
PPP
HTTP
TCP Header
IP Header
http request/response may include a large amount of data
TCP provides connection management and reliable delivery
IP provides machine to machine delivery, may segment data
Point-to-Point Protocol provide delivery from one machine to next. may compress, modify, encrypt data, etc.

## Slide 15
Please attribute Dr. Jim Alves-Foss and Dr. Jia Song, University of Idaho
Except where otherwise noted, this work is licensed under https://creativecommons.org/licenses/by-nc-sa/4.0/ Not withstanding the non-commercial license terms, non-profit educational institutions are granted a non-exclusive license to adapt and use this material, with attribution. Creative Commons and the double C in a circle are registered trademarks of Creative commons in the United States and other countries. Third party marks and brands are the property of their respective holders.
Project sponsored by the National Security Agency under grant Number H98230-17-1-0199. The United States Government is authorized to reproduce and distribute reprints notwithstanding any copyright notation herein.