## Slide 1: Module 1: Internetworking
Lesson 1: Internetworking

## Slide 2: Internetworking Module
Module Description: ​
The intent of this Knowledge Unit is to provide students with an understanding of networking and internet protocols.
Topics:​
  Lesson 1: Networking Overview​
  Lesson 2: Internetworking
  Lesson 3: PCAP File Format

## Slide 3: Learning Outcomes
Upon completion of this lesson, students will be able to:
  Students will be able to describe and discuss data network architectures and protocols, including UDP, TCP and IP protocols.
  Students will be able to track and identify the packets involved in a simple TCP connection (or a trace of such a connection).

## Slide 4: Background
What are networked systems?
  A set of devices (hosts) connected by a communication medium that are able to share data through transmission over the media
  System Characteristics include (but are not limited to)
    Physical properties of the communication signals
    Physical topology of the communication medium and logical topology of the data transmission
    Format and timing of the signals
    Error and Flow control, connection management, recovery, security

## Slide 5: Internetworking
What/Why and How?
  What is internetworking?
    It is the mechanism that permits users attached to different autonomous (independently managed and implemented) networks (either LAN or WAN) to communicate with each other.
    It provides seamless integration of the communication, providing an abstract view of the internetwork independent of the underlying physical or logical topology.

## Slide 6: Internetworking
  Why?
    For the same reasons we network locally. To share information and resources in an efficient manner.
  How?
    Autonomous networks connect through Intermediate Systems (ISs) that are members of two or more of the networks.

## Slide 7: Internetworking
Major issues behind internetworking
  Network Service:
    Networks attached to an internetwork may consist of connectionless LANs and connection oriented WANs.
    Each network may have different delay rates, error control mechanisms, etc.
    Protocol must integrate these services into a standard user interface

## Slide 8: Internetworking
  Addressing
    The NPA (network point of attachment) is a unique network wide identifier to address a particular user.
    Naming structure may be different per network
    Need an Open System Internetworking Environment (OSIE) with internetwork-wide addressing and name resolution (based on unique NSAPs = network service attachment point)

## Slide 9: Internetworking
  Routing
    ES = end-system (host); NPS = (Network address); IS = (Intermediate system/Gateway)
    How does ES determine NPA address(es) of IS(s) attached to its network?
    How does an IS determine NPA address of ESs attached to its network?
    How does an ES select a specific IS when sending an NPDU?
    How does an IS determine the NPA addresses of other ISs that are attached to the same network?
    How does an IS select a specific IS to route an NPDU to a given destination ES?

## Slide 10: Internetworking
  Quality of Service
    Each network allows user to specify a set of expected performance parameters (transit delay; security; cost limits; expected residual error rate; priority)
    These QOS parameters may be different for different networks
    Must provide a means of letting each network entity build of knowledge of internetwork-wide QOS to be expected when going to any destination NSAP
    How does this work over networks with different size constraints?

## Slide 11: Internetworking
  Maximum Packet Size
    Affected by error rates, transit delay, buffer limits, processing overhead (128-8000+ bytes are typical)
    Each network has a maximum specified for transport layer to divide TPDU into segments or fragments.
  Flow and Congestion Control
    Completely different mechanisms are used for connection-oriented and connectionless networks
    Must integrate these mechanisms to provide for internetwork-wide error and flow control
  Error Reporting
    Varies from one network type to another
    A global scheme must be established to integrate these

## Slide 12: Internetworking
The Internet Protocol (IP)
  RFC 791 https://tools.ietf.org/html/rfc791
  Read the RFC, it is the official standard. Can you follow it?
  1.1. Motivation
    The Internet Protocol is designed for use in interconnected systems of packet-switched computer communication networks. Such a system has been called a "catenet" [1]. The Internet protocol provides for transmitting blocks of data called datagrams from sources to destinations, where sources and destinations are hosts identified by fixed length addresses. The Internet protocol also provides for fragmentation and reassembly of long datagrams, if necessary, for transmission through "small packet" networks.

## Slide 13: Internetworking
  1.2. Scope
    The Internet protocol is specifically limited in scope to provide the functions necessary to deliver a package of bits (an Internet datagram) from a source to a destination over an interconnected system of networks. There are no mechanisms to augment end-to-end data reliability, flow control, sequencing, or other services commonly found in host-to-host protocols. The Internet protocol can capitalize on the services of its supporting networks to provide various types and qualities of service.
  1.3. Interfaces
    This protocol is called on by host-to-host protocols in an Internet environment. This protocol calls on local network protocols to carry the Internet datagram to the next gateway or destination host.

## Slide 14: Internetworking
  Where does IP fit?
Local Network Protocol
Internet Protocol (IP) & ICMP
TCP
UDP
Telnet
HTTP
FTP

## Slide 15: Internetworking
Network Addresses are 32 bits in IPV4
  Class A (for large independent networks) they are indexed with a 7 bit netid and a 24 bit hostid (bit 1 = 0)
  Class B (for corporate-wide networks) they are indexed with a 14 bit netid and a 16 bit netid (bits 1,2 = 1,0).
  Class C (for single small LANs) they are indexed with a 21 bits netid and an 8 bit hostid (bits 1-3 = 1,1,0). Note: many agencies locally divide their Class B into subnets similar to Class C (based on a subnet mask, where 1’s are used to indicate valid netid portion)
  Class D multicast (bits 1-4 = 1,1,1,0) remaining 28 are group id.
    all 1’s usually all-station broadcast, although address with bits 1-4 = 1,1,1,1 is technically reserved

## Slide 16: Internetworking
Network Addresses Continued:
  Usually represented with dotted-decimal notation: 10.0.0.0 = Arpanet; 129.101.100.1 = machine 1 on subnet 100 or machine 100.1 of Class B network 129.101
  A local network may combine different LAN types (at the network layer), thus causing routers to be used and each network to have a unique net_id. The subnetworking of Class B networks is used to help reduce workload on ISs (routers/bridges) that combine the site-wide network into a single LAN. If not decoupled, each would be involved in overall internet routing.
  Single gateway from site provides internetwork-wide routing, internally the subnetwork routing is handled.

## Slide 17: Internetworking
The IP NPDU: (see the RFC)
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|Version| IHL |Type of Service| Total Length |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Identification |Flags| Fragment Offset |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Time to Live | Protocol | Header Checksum |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Source Address |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Destination Address |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Options | Padding |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Example Internet Datagram Header

## Slide 18: Fields
Version: (4 bits) – currently version 4 or 6
IHL: (4 bits) - number of 32 bit words in header
Type of Service (8 bits) - (QOS – next slide)
Total Length (16 bits) - number bytes in total IP packet (header+ data)
Identification (16 bits) – “unique per datagram”
Flags (3 bits) – see later slide
Fragment Offset (13 bits) – number of bytes (octets) from beginning

## Slide 19: Fields (con’t)
Time to live (8 bits) – number of “hops”
Protocol (8 bits) – next layer (see later slide)
Header Checksum (16 bits)
  one’s complement of one’s complement sum of headers 16 bit words (assuming this field 0).
  If we sum whole header w/checksum; result should be 0

## Slide 20: Internetworking
QOS Fields
  Bits 0-2: Precedence.
0 1 2 3 4 5 6 7
+-----+-----+-----+-----+-----+-----+-----+-----+
| | | | | | |
| PRECEDENCE | D | T | R | 0 | 0 |
| | | | | | |
+-----+-----+-----+-----+-----+-----+-----+-----+
    Precedence:
    111 - Network Control 110 - Internetwork Control
    101 - CRITIC/ECP 100 - Flash Override
    011 - Flash 010 - Immediate
    001 - Priority 000 - Routine

## Slide 21: Internetworking
QOS Fields
  Bit 3: 0 = Normal Delay, 1 = Low Delay.
  Bits 4: 0 = Normal Throughput, 1 = High Throughput.
  Bits 5: 0 = Normal Reliability, 1 = High Reliability.
  Bit 6-7: Reserved for Future Use.

## Slide 22: Internetworking
Flags:
  Various Control Flags.
  Bit 0: reserved, must be zero
  Bit 1: (DF) 0 = May Fragment, 1 = Don't Fragment.
  Bit 2: (MF) 0 = Last Fragment, 1 = More Fragments.
0 1 2
+---+---+---+
| | D | M |
| 0 | F | F |
+---+---+---+

## Slide 23: IP Protocol Field
See Examples below and full list at:
https://www.iana.org/assignments/protocol-numbers/protocol-numbers.xhtml
Protocol Number | Protocol Name
1 | ICMP
2 | IGMP
3 | GGP
4 | IP-in-IP
5 | ST
6 | TCP
8 | EGP
17 | UDP

## Slide 24: Ex: tcpdump (-nx –r xxx.pcap)
22:01:59.517328 IP 127.76.210.185.2507 > 127.0.0.1.10391: Flags [.], ack 507, win 350,
options [nop,nop,TS val 4294941147 ecr 4294941147], length 0
0x0000: 4500 0034 3b42 4000 4006 2e7b 7f4c d2b9
0x0010: 7f00 0001 09cb 2897 2ae5 a46c ce57 538b
0x0020: 8010 015e d12d 0000 0101 080a ffff 99db
0x000: ffff 99db
Version
IHL
QOS
Total Length
Identification
Flags
Fragment Offset
Time to Live
Protocol
Checksum
SRC IP
DST IP

## Slide 25: Internetworking
IP protocol Functions:
  Fragmentation and Reassembly
    The IP protocol permits a user to submit a TPDU (NSDU) up to 64Kbytes in size. However, member networks may not be able to handle such large packets. IP provides a mechanism for dividing the packets into smaller fragments when needed and reassembling them before delivery. There are two possible techniques:
      Internet Fragmentation
      Intranet Fragmentation

## Slide 26: Internetworking
  Intranet fragmentation - This technique requires that a companion network that forces a fragmentation does so only locally and reassembles the packet before passing it on to the next member network.
    Always utilizes the maximum size packet possible
    More overhead, processing delay and buffering required.
  Internet Fragmentation - This technique keeps packets fragmented until they arrive at final destination (IP uses this with a time-to-live option)
    No extra overhead or buffering in intermediate nodes
    May not be very efficient use of network bandwidth

## Slide 27: Internetworking
Routing:
  To move datagrams across multiple networks, from the source to the destination, we need a routing mechanism.
    Centralized routing - based on the concept of a central repository that maintains routing information for all machine on the internet
    Distributed routing - based on the concept that the routing information is strategically distributed across the network

## Slide 28: Internetworking
The routing is performed by gateways (or routers)
  Interior Gateways - configured to route packets within a local (or corporate-wide) network -- a single autonomous network.
  Exterior Gateways - configured to route packets between autonomous networks to other exterior gateways and transfer information between attached autonomous network and core network

## Slide 29: Internetworking
ARP (Address Resolution Protocol)
  Basic routing requires that we send a message to the interior gateway attached to our subnetwork and ask it to forward the message to the destination.
    This is horribly inefficient for messages to hosts on the same subnetwork. We want local IP agent to know that destination is on same subnetwork and transmit packet to that NPA directly.
    ARP is a protocol that allows us to do that:
      Broadcast an ARP request packet with own IP/NPA address, and requested target IP address.
      Receive a response from target with correct IP/NPA address.
      This information is cached.

## Slide 30: Internetworking
  Example run of arp (with -a “archive” option)
    brownlee:jimaf:21>/etc/arp -a
    dworshak.cs.uidaho.edu (129.101.120.160) at 8:0:9:41:ee:53 ether
    panther.cs.uidaho.edu (129.101.100.65) at 8:0:2b:1b:ca:37 ether
    iris.cs.uidaho.edu (129.101.120.129) at 8:0:69:7:e5:5a ether
    coffee.cs.uidaho.edu (129.101.100.131) at 8:0:9:62:c2:85 ether
    leopard.cs.uidaho.edu (129.101.100.67) at 8:0:9:17:fa:15 ether
    puffin.cs.uidaho.edu (129.101.100.100) at (incomplete)
    indigo.cs.uidaho.edu (129.101.100.132) at 8:0:9:62:e:68 ether
    tadpole.cs.uidaho.edu (129.101.120.69) at 8:0:9:60:bb:0 ether
    teapot.cs.uidaho.edu (129.101.120.78) at 8:0:9:70:e:b2 ether
    spangle.cs.uidaho.edu (129.101.120.79) at 8:0:9:49:81:6a ether
    bayhorse.cs.uidaho.edu (129.101.120.80) at 8:0:9:70:f1:a0 ether
    cascade.cs.uidaho.edu (129.101.100.17) at 8:0:9:3d:e9:e5 ether
    boulder.cs.uidaho.edu (129.101.120.81) at 8:0:9:70:11:7a ether
    hidden.cs.uidaho.edu (129.101.120.82) at 8:0:9:70:9:f2 ether
    lava.cs.uidaho.edu (129.101.100.19) at 8:0:9:70:1e:12 ether
    crater.cs.uidaho.edu (129.101.120.83) at 8:0:9:70:a9:89 ether

## Slide 31: Internetworking
Interior Gateway Protocols (IGP)
  Most commonly used is IP routing information protocol (RIP)
    Distributed routing protocol based on a distance vector algorithm
    Distance is usually measured in terms of hops (or some other metric such as delay). An interior gateway uses hop counts to determine distance between itself an all other subnetworks on the same autonomous system; information is stored in remote routing table.
    Initially (configuration time) only information stored is that of attached networks and adjacent gateways
    Periodically IGs send full table to adjacent neighbors to dynamically update tables:
      not all tables will have same information
      large overhead for large networks

## Slide 32: Internetworking
Exterior Gateway Protocol (EGP)
  Uses a reachability table to permit it to contact all other EGs in the core network.
  Three main functions:
    neighbor acquisition: two EGs agree to exchange routing information
    neighbor reachability: confirm relationship with hello and I-heard-you messages
    routing update: exchange information from known reachability table with poll messages
    See figure 9.16 pg 464 of the text and handouts

## Slide 33: Internetworking
Internet Control Message Protocol (ICMP)
  Full description is in supplemental readings
    Error Reporting
    Reachability Testing
    Congestion Control
    Route-change Notification
    Performance Measuring
    Subnet Addressing
      0 = Echo Reply; 3 = Destination Unreachable; 4 = Source Quench;
      5 = Redirect; 8 = Echo; 11 = Time Exceeded; 12 = Parameter Problem; 13 = Timestamp; 14 = Timestamp Reply; 15 = Information Request;
      16 = Information Reply

## Slide 34: Internetworking
ICMP
  The purpose behind the use of ICMP is to permit the transfer of control messages between IP agents to enable a more robust and trustworthy network layer
  Use:
    It is a type 1 message using the lower IP layer header
    The data part of the IP datagram is the ICMP Datagram which consists of:
      Type = 1 byte specifying ICMP message content
      Code = 1 byte specifying subtype
      Checksum (16 bit ones complement of ICMP message)
      n*32 bits ICMP type specific fields
      (See optional reading for details)

## Slide 35: The Transport Layer
The Transport Layer
  Provides reliable end-to-end communication between processes on hosts. Ensures error-free delivery and sequencing and provides connection management. (DoD’s TCP best known).
  This is the keystone of the whole concept of a computer-communications architecture. This is the layer that provides end-to-end communication between user processes over machines attached to a network.
    Lower level protocols are better understood and, on the whole, are less complex than transport protocols. Also standard have settled out for most kinds of layer 103 transmission facilities.
    Upper levels are less important in that applications can directly access the services of the transport level and avoid presentation and session layers

## Slide 36: The Transport Layer
Transport Layer Services
  Type of Service
    Connection Oriented and/or Connectionless
    Establishment, maintenance and termination of a logical connection between transport users. Most common type of protocol service provided. Provides error and flow control
    However, Connectionless is useful
      periodic or passive sampling of data (such as sensors)
      broadcasts of messages to network users
      request-response (client/server) applications in which a transaction service is provided by a common server to a number of distributed users
      real-time applications: such as voice and telemetry involving a degree of redundancy and/or real-time transmission requirements

## Slide 37: The Transport Layer
  Quality of Service
    A transport layer may provide ability for user to select/specify
      Acceptable error and loss levels
      Desired average and maximum delay
      Desired average and minimum throughput
      Priority Levels
    Of course transport layer limited to inherent capabilities of underlying network service provided - therefore the transport layer will have varying degrees of success in providing the requested service
    One method of providing this service is to provide different transport protocols for different classes of traffic:
      1) A reliable connection-oriented protocol 2) A less reliable connection-oriented protocol 3) A speech protocol, requiring sequenced, timely delivery 4) A real-time protocol requiring high reliability and timeliness

## Slide 38: The Transport Layer
  Data Transfer
    The whole purpose of the transport layer is of course to provide transport of data between two transport entities
    User and control data can be on same or separate channels
    Full-duplex must be supported although half-duplex and simplex may also be offered for special situations
  User Interface
    This may be application/environment
    Could be:
      Procedure calls
      Passing of data and parameters to a process through a mailbox
      Use of DMA
    Common interface would be for flow control with transport users; timing; confirmation significance (local or remote)

## Slide 39: The Transport Layer
  Connection Management
    Needs to be responsible for connection establishment and termination (for connection oriented services)
    A symmetric and an asymmetric service should be provided
    Termination can be abrupt or graceful
  Expedited Delivery
    This permits data to supersede the transport of data in the local agents queue
  Status Reporting
    Performance characteristics (throughput, mean delay); addresses (network, transport); class of protocol in use; current timer values; state of protocol “machine” supporting a connection; degradation in requested quality of service
  Security - Of course, another fine service

## Slide 40: Transport Layer
User Datagram Protocol
  Recall that the IP protocol provides a connectionless datagram service to users with no implicit error or flow control mechanism
  To permit users to use this level of service, the User Datagram Protocol (UDP) was established
      This User Datagram Protocol (UDP) is defined to make available a datagram mode of packet-switched computer communication in the environment of an interconnected set of computer networks. This protocol assumes that the Internet Protocol (IP) is used as the underlying protocol.
      This protocol provides a procedure for application programs to send messages to other programs with a minimum of protocol mechanism. The protocol is transaction oriented, and delivery and duplicate protection are not guaranteed.

## Slide 41: Transport Layer
A UDP Protocol Data Unit:
    Source Port- an optional field, when meaningful it indicates the port of the sending process, and may be assume to be the port to which a reply should be sent. If not used, a value of zero is indicated
    Destination Port - has meaning within the context of a particular internet destination address
    Length - is number of octets of the user datagram including the header
    Checksum is 16-bit one complement of the one’s complement sum of a pseudo header of IP layer info and UDP header info.
Source Port (16 bits)
Destination Port (16 bits)
Length (16 bits)
Checksum (16 bits)

## Slide 42: Transport Layer
What is a port?
  As you have seen in the UDP header we have what we call a source and destination port address. These are the addresses used by the transport layer users to permit a transport layer to service multiple users.
  Ports are used by both TCP and UDP to indicate unique process addresses (similar to ISO service access point or address selector)
  A fully qualified TCP/IP or UDP/IP address often looks like: 129.101.100.66:25 or 129.101.100.66,15
  In the above examples, which is a UDP and which is a TCP address?

## Slide 43: Transport Layer
UDP User (Interface Services)
  the creation of new receive ports,
  receive operations on the receive ports that return the data octets and an indication of source port and source address,
  an operation that allows a datagram to be sent, specifying the data, source and destination ports and addresses to be sent.

## Slide 44: Transport Layer
Network Layer (IP) interface
  The UDP module must be able to determine the source and destination internet addresses and the protocol field from the internet header. One possible UDP/IP interface would return the whole internet datagram including all of the internet header in response to a receive operation. Such an interface would also allow the UDP to pass a full internet datagram complete with header to the IP to send. The IP would verify certain fields for consistency and compute the internet header checksum.
  It is protocol #17 (21 octal) when used in conjunction with IP

## Slide 45: Transport Layer
The Transmission Control Protocol (TCP)
  As mentioned previously, the transport layer is at a unique position of being close enough to the network layer and yet high enough to provide full end-to-end connectivity for users. It is a this position that it is logical to provide full end-to-end error and flow control capabilities.
  The Transmission Control Protocol (TCP) is intended for use as a highly reliable host-to-host protocol between hosts in packet-switched computer communication networks, and in interconnected systems of such networks.

## Slide 46: Transport Layer
Motivation
  TCP is a connection-oriented, end-to-end reliable protocol designed to fit into a layered hierarchy of protocols which support multi-network applications. The TCP provides for reliable inter-process communication between pairs of processes in host computers attached to distinct but interconnected computer communication networks. Very few assumptions are made as to the reliability of the communication protocols below the TCP layer. TCP assumes it can obtain a simple, potentially unreliable datagram service from the lower level protocols. In principle, the TCP should be able to operate above a wide spectrum of communication systems ranging from hard-wired connections to packet-switched or circuit-switched networks.

## Slide 47: Transport Layer
Services Provided:
  Basic Data Transfer:
    The TCP is able to transfer a continuous stream of octets in each direction between its users by packaging some number of octets into segments for transmission through the internet system. In general, the TCPs decide when to block and forward data at their own convenience.
    Sometimes users need to be sure that all the data they have submitted to the TCP has been transmitted. For this purpose a push function is defined. To assure that data submitted to a TCP is actually transmitted the sending user indicates that it should be pushed through to the receiving user. A push causes the TCPs to promptly forward and deliver data up to that point to the receiver. The exact push point might not be visible to the receiving user and the push function does not supply a record boundary marker.

## Slide 48: Transport Layer
  Reliability
    The TCP must recover from data that is damaged, lost, duplicated, or delivered out of order by the internet communication system. This is achieved by assigning a sequence number to each octet transmitted, and requiring a positive acknowledgment (ACK) from the receiving TCP. If the ACK is not received within a timeout interval, the data is retransmitted. At the receiver, the sequence numbers are used to correctly order segments that may be received out of order and to eliminate duplicates. Damage is handled by adding a checksum to each segment transmitted, checking it at the receiver, and discarding damaged segments.
    As long as the TCPs continue to function properly and the internet system does not become completely partitioned, no transmission errors will affect the correct delivery of data. TCP recovers from internet communication system errors.

## Slide 49: Transport Layer
  Flow Control
    TCP provides a means for the receiver to govern the amount of data sent by the sender. This is achieved by returning a "window" with every ACK indicating a range of acceptable sequence numbers beyond the last segment successfully received. The window indicates an allowed number of octets that the sender may transmit before receiving further permission.

## Slide 50: Transport Layer
  Multiplexing
    To allow for many processes within a single Host to use TCP communication facilities simultaneously, the TCP provides a set of addresses or ports within each host. Concatenated with the network and host addresses from the internet communication layer, this forms a socket. A pair of sockets uniquely identifies each connection. That is, a socket may be simultaneously used in multiple connections.
    The binding of ports to processes is handled independently by each Host. However, it proves useful to attach frequently used processes (e.g., a "logger" or timesharing service) to fixed sockets which are made known to the public. These services can then be accessed through the known addresses. Establishing and learning the port addresses of other processes may involve more dynamic mechanisms.

## Slide 51: Transport Layer
  Connections
    The reliability and flow control mechanisms described above require that TCPs initialize and maintain certain status information for each data stream. The combination of this information, including sockets, sequence numbers, and window sizes, is called a connection. Each connection is uniquely specified by a pair of sockets identifying its two sides.
    When two processes wish to communicate, their TCP's must first establish a connection (initialize the status information on each side). When their communication is complete, the connection is terminated or closed to free the resources for other uses.
    Since connections must be established between unreliable hosts and over the unreliable internet communication system, a handshake mechanism with clock-based sequence numbers is used to avoid erroneous initialization of connections.

## Slide 52: Transport Layer
  Precedence and Security
    The users of TCP may indicate the security and precedence of their communication. Provision is made for default values to be used when these features are not needed.

## Slide 53: Transport Layer
Service Primitives:
    UNSPECIFIED_PASSIVE_OPEN (Request by server)
      Source Port, Timeout, Timeout-Action, Precedence, Security Range
    FULL_PASSIVE_OPEN (Request by server)
      Local Connection Name , Timeout, Timeout-Action, Precedence, Security Range
    ACTIVE_OPEN (Request by client)
      Source Port, Destination Port, Destination Address, Timeout, Timeout-Action, Precedence, Security Range
    ACTIVE_OPEN_WITH_DATA (Request by client)
      Source Port, Destination Port, Destination Address, Data, Data Length, Push Flag, Urgent Flag, Timeout, Timeout-Action, Precedence, Security Range
    OPEN_ID (Local Response to Client)
      Local Connection Name, Source Port, Destination Port/Address

## Slide 54: Transport Layer
    OPEN_SUCCESS (Confirm to Client)
      Local Connection Name
    OPEN_FAILURE (Confirm to Client)
      Local Connection Name
    SEND (Request from client/server)
      Local Connection Name, Data, Data Length, Urgent Flag, Timeout, Timeout-Action
    DELIVER (Indication to client/server)
      Local Connection Name, Data, Data Length, Urgent Flag
    ALLOCATE (Request from client/server)
      Local Connection Name, Data Length
    CLOSE (Request from client/server)
      Local Connection Name
    CLOSING (Indication to client/server)
      Local Connection Name

## Slide 55: Transport Layer
    TERMINATE (Confirm from client/server)
      Local Connection Name, Reason Code
    ABORT (Request from client/server)
      Local Connection Name
    STATUS (Request from client/server)
      Local Connection Name
    STATUS_RESPONSE (Local response to client/server)
      Local Connection Name, Source Port/Address, Destination Port/Address, Connection State, Receive Window, Send Window, Waiting ACK, Waiting Receipt, Urgent, Precedence, Security, Timeout
    ERROR (Local indication to client/server)
      Local Connection Name, Reason Code

## Slide 56: Transport Layer
TCP Protocol Data Unit
Source Port
Destination Port
Acknowledgment Number
Checksum
Sequence Number
Offset
Reserved
Flags
Window
Urgent Pointer
Options
Padding
32 bits

## Slide 57: Ex: tcpdump (-nx –r xxx.pcap)
22:01:59.517328 IP 127.76.210.185.2507 > 127.0.0.1.10391: Flags [.], ack 507, win 350,
options [nop,nop,TS val 4294941147 ecr 4294941147], length 0
0x0000: 4500 0034 3b42 4000 4006 2e7b 7f4c d2b9
0x0010: 7f00 0001 09cb 2897 2ae5 a46c ce57 538b
0x0020: 8010 015e d12d 0000 0101 080a ffff 99db
0x0040: ffff 99db
SRC Port
DST Port
Checksum
SEQ Number
ACK Number

## Slide 58: Transport Layer
  Source Port: 16 bits
    The source port number.
  Destination Port: 16 bits
    The destination port number.
  Sequence Number: 32 bits
    The sequence number of the first data octet in this segment (except when SYN is present). If SYN is present the sequence number is the initial sequence number (ISN) and the first data octet is ISN+1.
  Acknowledgment Number: 32 bits
    If the ACK control bit is set this field contains the value of the next sequence number the sender of the segment is expecting to receive. Once a connection is established this is always sent.
  Data Offset: 4 bits
    The number of 32 bit words in the TCP Header. This indicates where the data begins. The TCP header (even one including options) is an integral number of 32 bits long.

## Slide 59: Transport Layer
  Reserved: 6 bits
    Reserved for future use. Must be zero.
  Control Bits: 6 bits (from left to right):
    URG: Urgent Pointer field significant
    ACK: Acknowledgment field significant
    PSH: Push Function
    RST: Reset the connection
    SYN: Synchronize sequence numbers
    FIN: No more data from sender
  Window: 16 bits
    The number of data octets beginning with the one indicated in the acknowledgment field which the sender of this segment is willing to accept.

## Slide 60: Transport Layer
  Checksum: 16 bits
    The checksum field is the 16 bit one's complement of the one's complement sum of all 16 bit words in the header and text. If a segment contains an odd number of header and text octets to be checksummed, the last octet is padded on the right with zeros to form a 16 bit word for checksum purposes. The pad is not transmitted as part of the segment. While computing the checksum, the checksum field itself is replaced with zeros. The checksum also covers a 96 bit pseudo header conceptually prefixed to the TCP header. This pseudo header contains the Source Address, the Destination Address, the Protocol, and TCP length. This gives the TCP protection against misrouted segments. This information is carried in the Internet Protocol and is transferred across the TCP/Network interface in the arguments or results of calls by the TCP on the IP.
    The TCP Length is the TCP header length plus the data length in octets (this is not an explicitly transmitted quantity, but is computed), and it does not count the 12 octets of the pseudo header.

## Slide 61: Transport Layer
  Urgent Pointer: 16 bits
    This field communicates the current value of the urgent pointer as a positive offset from the sequence number in this segment. The urgent pointer points to the sequence number of the octet following the urgent data. This field is only interpreted in segments with the URG bit set.
  Options: variable
    Options may occupy space at the end of the TCP header and are a multiple of 8 bits in length. All options are included in the checksum. An option may begin on any octet boundary. There are two cases for the format of an option:
      Case 1: A single octet of option-kind.
      Case 2: An octet of option-kind, an octet of option-length, and the actual option-data octets.
    The option-length counts the two octets of option-kind and option-length as well as the option-data octets. Note that the list of options may be shorter than the data offset field might imply. The content of the header beyond the End-of-Option option must be header padding.

## Slide 62: Ex: tcpdump (-nx –r xxx.pcap)
22:01:59.517328 IP 127.76.210.185.2507 > 127.0.0.1.10391: Flags [.], ack 507, win 350,
options [nop,nop,TS val 4294941147 ecr 4294941147], length 0
0x0000: 4500 0034 3b42 4000 4006 2e7b 7f4c d2b9
0x0010: 7f00 0001 09cb 2897 2ae5 a46c ce57 538b
0x0020: 8010 015e d12d 0000 0101 080a ffff 99db
0x0030: ffff 99db
Version
IHL
QOS
Total Length
Identification
Flags
Fragment Offset
Time to Live
Protocol
Checksum
SRC IP
DST IP

## Slide 63: Transport Layer
TCP Operation:
  Connection Establishment:
    Uses a threeway handshake. Each side sends an initial sequence number (indicated by setting the SYN bit)
  Data Transfer
    Uses HDLC-like sliding window and GO-BACK-N protocols
    Allows use of PUSH and URGENT flags
    Can recover from errors due to crashes or old duplicate SYNs by use of RST command
  Connection Termination
    Graceful request for termination (Setting the FIN flag)
    Response may contain data.

## Slide 64: Transport Layer
TCP Implementation Policy Options
  Send Policy
    In absence of a closed transmission window or pushed data, the sending TCP entity is free to transmit data at its own convenience; actual policy depends on performance characteristics
  Deliver Policy
    In the absence of a push, a receiving TCP entity is free to deliver data to user at its own convenience
  Accept Policy
    When all data segments arrive in order over TCP connection, the data is placed in receive buffers to be sent to the user. However, if they arrive out-of-order
      In-order - accept only those that arrive in order; discard others
      In-window - accept all segments within receive window

## Slide 65: Transport Layer
Retransmission Policy
  TCP maintains a queue of segments that have been sent but not yet acknowledged. A retransmit occurs after time-out
    First-only - Maintain one retransmission timer for entire queue. If ACK is received, remove appropriate segment(s) and reset timer. If timer expires, retransmit first segment and reset timer
    Batch- Maintain one retransmission timer for entire queue. If ACK is received, remove appropriate segment(s) and reset timer. If timer expires, retransmit all segments in the queue and reset timer
    Individual - Maintain one retransmission timer for each segment in the queue. If ACK is received, remove appropriate segment(s) and destroy corresponding timer(s). If timer expires, retransmit corresponding segment individually and reset timer

## Slide 66: Transport Layer
Acknowledgment Policy
  When data arrives that is in sequence, receiving TCP has two options concerning timing of acknowledgment
    Immediate - When data are accepted, immediately transmit an empty (no data) segment containing the appropriate acknowledgment number
    Cumulative - When data are accepted, record the need for acknowledgment, but wait for an outbound segment with data on which to piggyback the acknowledgment. To avoid long delay, set a window timer; if timer expires before acknowledgment is sent, transmit and empty segment containing the appropriate acknowledgment number.

## Slide 67
Please attribute Dr. Jim Alves-Foss and Dr. Jia Song, University of Idaho
Except where otherwise noted, this work is licensed under https://creativecommons.org/licenses/by-nc-sa/4.0/ Not withstanding the non-commercial license terms, non-profit educational institutions are granted a non-exclusive license to adapt and use this material, with attribution. Creative Commons and the double C in a circle are registered trademarks of Creative commons in the United States and other countries. Third party marks and brands are the property of their respective holders.
Project sponsored by the National Security Agency under grant Number H98230-17-1-0199. The United States Government is authorized to reproduce and distribute reprints notwithstanding any copyright notation herein.