## Slide 1: Module 0: Introduction
Lesson 2: Intel Assembly

## Slide 2: Learning Outcomes
Upon completion of this lesson, students will be able to
  Read and interpret basic intel assembly
  Discuss intel assembly format

## Slide 3: Introduction
Intel Assembly (IA-32)
  Intel’s official manuals:
    https://software.intel.com/en-us/articles/intel-sdm
    There are over 1000 different instructions in the intel assembly language.
    You want Volume 2 Instruction Set Reference
    This is over 2000 pages long for the combined IA-64 and IA-32
  Intel is the most common personal computer architecture
  IA-32 refers to the 32-bit version of the intel assembly language.
  IA-64 refers to the 64-bit version of the intel assembly language, and is backwards compatible to IA-32
  Other names you may see: x86, x86-32, i386

## Slide 4: Notation
There are two common notation forms for intel assembly:
AT&T
  Source operand precedes destination operand
  Used commonly in older tools (gcc, gdb, ..)
  Examples:
    mov $0x4, %eax // store the immediate value in register “eax”
    mov %(eax), %ebx // treat register eax as a pointer and move contents
        // pointed to register “ebx”
Intel
  Destination precedes source
  mov eax, 4
  mov ebx, [eax]
Warning: the human readable operation name, the mnemonic sometimes differs between the two

## Slide 5: Notational Conventions
Bit and Byte Order
  Intel is a “little endian machine”. Bytes of a word are stored with least significant byte first.
Reserved bits
  Some bits are reserved, and should not be used
Mnemonics and operands
  Some instructions will have labels, or use label to refer to specific addresses in memory.

## Slide 6: Registers
Intel has several different groups of registers
  These are “processor” memory and are accessed very quickly.
  Can be used as “variables” for the code
  Are addressed by name in the code
  Groups include
    Data registers
    Address registers
    Conditional registers
    General purpose registers
    Special purpose registers
    Floating point registers
    Vector arithmetic registers
    …

## Slide 7: IA-32 General Purpose Registers
General purpose registers are 32-bits wide, and portion can be accessed through special names
32-bit name | Lower 16 bits | High byte of lower 16 bits | Low byte of lower 16 bits | Use
eax | ax | ah | al | General storage, accumulator, results
ebx | bx | bh | bl | General storage, base pointer for data is DS segment
ecx | cx | ch | cl | General storage, counter
edx | dx | dh | dl | General storage, data, I/O pointer
esi | si | -- | -- | General storage, pointer for memory copying operations, source index
edi | di | -- | -- | General storage, pointer for memory copying operations, destination index
ebp | bp | -- | -- | Stack “base pointer”
esp | sp | -- | -- | “stack pointer”

## Slide 8: IA-32 Special Registers
EIP (extending instruction pointer)
  Program counter
  32-bit address for next instruction
  Altered by special instructions, not directly by programmer
    JMP, Jcc, CALL, RET, IRET
  Control flow attacks focus on controlling this register
Status Control Register (EFLAGS)
  Basis for conditional control flow
    CF (carry flag), PF (parity flag), ZF (zero flag), SF (sign flag), OF (overflow flag)
  Processor status

## Slide 9: IA-32 Segmented memory model
In general not used.
Special registers
  CS – code segment, DS – data segments, SS stack segment
  ES, FS, GS – extra data segments
  In 64-bit mode, CS, DS, SS and ES are forced to 0
Segment registers contain 16 bits
  These are pointers into a segment table which gives the start address of a segment. All other addresses are treated as offsets.
  mov ss:[edx], es // moves value stored at SS address +edx

## Slide 10: IA-32 Other registers
Other register you may see
  Floating point (FPU) registers
    ST0-ST7, status word, control word, tag word, ..
  MMX (for vector operations)
    MM0-MM7 (64 bit registers)
    XMM0-XMM7 (128 bit registers)
  Control Registers
    CR0, CR1, CR2, CR3
  Debug Registers
    DR0, DR1, DR2, DR3, DR6, DR7
  System Table Pointer Registers
    GDTR, LDTR, IDTR, task register

## Slide 11: Operands
Instructions operate on the following
  Registers
    EIP not allowed, others may be limited
    Some registers are implicit (EFLAGS may change but is not listed)
      add eax, ebx // (eax + ebx --> eax)
  Immediate (source operands only)
    These are literal, constant values (may refer to addresses)
      mov eax, 4
      mov byte ptr [0x0800404], 5 // move 5 into the byte a location 0x0800404
      jmp 0x400cc1 // jump to location 0x400cc1
  Memory references
    Operands can contain pointers to memory location
      mov [eax], 5

## Slide 12: Operand Addressing
Relative Offset Computation
  Access to an array
  Displacement can be none, 8, 16 or 32 bits
  Base is value in general purpose register
    (Pointer to start of array)
  Index is value in a general purpose register
    (Index of array)
  Scale
    (1,2,4 or 8) size of elements in array
  Offset (Address) =
    Base + (Index * Scale) + Displacement
    mov eax, [esi + ecx*4 + 4]

## Slide 13: Data Types
Byte (8 bits)
Word (16 bits)
Double word (32 bits)
Quadword (64 bits)
Double Quadword (128 bits)
To move a quad word from one xmm register to another:
  movq xmm1, xmm2
Unsigned:
  Intel does not normally differentiate between signed and unsigned integers, except in comparison operations

## Slide 14: Common Instructions -- Move
mov — Move (Opcodes: 88, 89, 8A, 8B, 8C, 8E, ...)
copies the data item referred to by its second operand (i.e. register contents, memory contents, or a constant value) into the location referred to by its first operand (i.e. a register or memory). While register-to-register moves are possible, direct memory-to-memory moves are not.
Syntax
  mov <reg>,<reg>
  mov <reg>,<mem>
  mov <mem>,<reg>
  mov <reg>,<const>
  mov <mem>,<const>
Examples
  mov eax, ebx — copy the value in ebx into eax
  mov byte ptr [var], 5 — store the value 5 into the byte at location var

## Slide 15: Push
push — Push stack (Opcodes: FF, 89, 8A, 8B, 8C, 8E, ...)
places its operand onto the top of the hardware supported stack in memory. Specifically, push first decrements ESP by 4, then places its operand into the contents of the 32-bit location at address [ESP]. ESP (the stack pointer) is decremented by push since the x86 stack grows down - i.e. the stack grows from high addresses to lower addresses.
Syntax
  push <reg32>
  push <mem>
  push <con32>
Examples
  push eax — push eax on the stack
  push [var] — push the 4 bytes at address var onto the stack

## Slide 16: Pop
pop — Pop stack
removes the 4-byte data element from the top of the hardware-supported stack into the specified operand (i.e. register or memory location). It first moves the 4 bytes located at memory location [SP] into the specified register or memory location, and then increments SP by 4.
Syntax
  pop <reg32>
  pop <mem>
Examples
  pop edi — pop the top element of the stack into EDI.
  pop [ebx] — pop the top element of the stack into memory at the four bytes starting at location EBX.

## Slide 17: LEA (Load Effective Address)
lea – load effective address
places the address specified by its second operand into the register specified by its first operand. Note, the contents of the memory location are not loaded, only the effective address is computed and placed into the register. This is useful for obtaining a pointer into a memory region.
Syntax
  lea <reg32>,<mem>
Examples
  lea edi, [ebx+4*esi] — the quantity EBX+4*ESI is placed in EDI.
  lea eax, [var] — the value in var is placed in EAX.
  lea eax, [val] — the value val is placed in EAX.
Hint:
  Fast way to also perform a calculation equivalent in form to base + (index*scale) + displacement

## Slide 18: NOP
nop – no operation (opcode 0x90)
  Does nothing, but handy placeholder, useful for shellcoding
  Can exist for alignment of functions
  Multibyte NOP:
Bytes | Assembly | Bytes
2 bytes | 66 NOP | 66 90H
3 bytes | NOP DWORD ptr [EAX] | 0F 1F 00H
4 bytes | NOP DWORD pte [EAX + 00H] | 0F !F 40 00H
5 bytes | NOP DWORD pte [EAX + EAX*1 + 00H] | 0F 1F 44 00 00H
6 bytes | 66 NOP DWORD pte [EAX + EAX*1 + 00H] | 66 0F 1F 44 00 00H
7 bytes | NOP DWORD ptr [EAX + 00000000H] | 0F 1F 80 00 00 00 00H
8 bytes | NOP DWORD ptr [EAX + EAX*1 + 00000000H] | 0F 1F 84 00 00 00 00 00H
9 bytes | 66 NOP DWORD ptr [EAX + EAX*1 + 00000000H] | 66 0F 1F 84 00 00 00 00 00H

## Slide 19: Arithmetic and Logic Instructions -- Addition
add — Integer Addition
adds together its two operands, storing the result in its first operand. Note, whereas both operands may be registers, at most one operand may be a memory location.
Syntax
  add <reg>,<reg>
  add <reg>,<mem>
  add <mem>,<reg>
  add <reg>,<con>
  add <mem>,<con>
Examples
  add eax, 10 — EAX ← EAX + 10
  add DWORD PTR [var], 10 — add 10 to the s32-bit value stored at memory address var

## Slide 20: Subtraction
sub — Integer Subtraction
stores in the value of its first operand the result of subtracting the value of its second operand from the value of its first operand.
Syntax
  sub <reg>,<reg>
  sub <reg>,<mem>
  sub <mem>,<reg>
  sub <reg>,<con>
  sub <mem>,<con>
Examples
  sub al, ah — AL ← AL - AH
  sub eax, 216 — subtract 216 from the value stored in EAX

## Slide 21: Increment and Decrement
inc, dec — Increment, Decrement
The inc increments the contents of its operand by one. The dec instruction decrements the contents of its operand by one.
Syntax
  inc <reg>
  inc <mem>
  dec <reg>
  dec <mem>
Examples
  dec eax — subtract one from the contents of EAX.
  inc DWORD PTR [var] — add one to the 32-bit integer stored at location var

## Slide 22: Integer Multiplication
imul — Integer Multiplication
two-operand form multiplies its two operands together and stores the result in the first operand. The result (i.e. first) operand must be a register.
three operand form multiplies its second and third operands together and stores the result in its first operand. Again, the result operand must be a register. Furthermore, the third operand is restricted to being a constant value.
Syntax
  imul <reg32>,<reg32>
  imul <reg32>,<mem>
  imul <reg32>,<reg32>,<con>
  imul <reg32>,<mem>,<con>
Examples
  imul eax, [var] — multiply the contents of EAX by the 32-bit contents of the memory location var. Store the result in EAX.
  imul esi, edi, 25 — ESI → EDI * 25

## Slide 23: Integer Division
idiv — Integer Division
divides the contents of the 64 bit integer EDX:EAX (constructed by viewing EDX as the most significant four bytes and EAX as the least significant four bytes) by the specified operand value. The quotient result of the division is stored into EAX, and remainder is placed in EDX.
Syntax
  idiv <reg32>
  idiv <mem>
Examples
  idiv ebx — divide the contents of EDX:EAX by the contents of EBX. Place the quotient in EAX and the remainder in EDX.
  idiv DWORD PTR [var] — divide the contents of EDX:EAX by the 32-bit value stored at memory location var. Place the quotient in EAX and the remainder in EDX.

## Slide 24: Bitwise logic
and, or, xor — Bitwise logical and, or and exclusive or
perform the specified logical operation (logical bitwise and, or, and exclusive or, respectively) on their operands, placing the result in the first operand location.
Syntax (<op> is and, or or xor)
  <op> <reg>,<reg>
  <op> <reg>,<mem>
  <op> <mem>,<reg>
  <op> <reg>,<con>
  <op> <mem>,<con>
Examples
  and eax, 0fH — clear all but the last 4 bits of EAX.
  xor eax, eax — set the contents of EAX to zero.

## Slide 25: Bitwise Logical not
not — Bitwise Logical Not
Logically negates the operand contents (that is, flips all bit values in the operand).
Syntax
  not <reg>
  not <mem>
Example
  not BYTE PTR [var] — negate all bits in the byte at the memory location var.

## Slide 26: Negation
neg — Negate
Performs the two's complement negation of the operand contents.
Syntax
  neg <reg>
  neg <mem>
Example
  neg eax — EAX → - EAX

## Slide 27: Shifting
shl, shr — Shift Left, Shift Right
shift the bits in their first operand's contents left and right, padding the resulting empty bit positions with zeros. The shifted operand can be shifted up to 31 places. The number of bits to shift is specified by the second operand, which can be either an 8-bit constant or the register CL. In either case, shifts counts of greater then 31 are performed modulo 32.
Syntax (<op> is either shl or shr)
  <op> <reg>,<con8>
  <op> <mem>,<con8>
  <op> <reg>,<cl>
  <op> <mem>,<cl>
Examples
  shl eax, 1 — Multiply the value of EAX by 2 (if the most significant bit is 0)
  shr ebx, cl — Store in EBX the floor of result of dividing the value of EBX by 2n wheren is the value in CL.

## Slide 28: Control Flow Instructions -- Jump
jmp — Jump
Transfers program control flow to the instruction at the memory location indicated by the operand.
Syntax
  jmp <label>
Example
  mov esi, [ebp+8]
  begin: xor ecx, ecx
  mov eax, [esi]
  jmp begin — Jump to the instruction labeled begin.

## Slide 29: Conditional jump
jcondition — Conditional Jump
Jump to label based on a condition in the control status word (EFLAGS)
Syntax
  je <label> (jump when equal)
  jne <label> (jump when not equal)
  jz <label> (jump when last result was zero)
  jg <label> (jump when greater than)
  jge <label> (jump when greater than or equal to)
  jl <label> (jump when less than)
  jle <label> (jump when less than or equal to)
Example
  cmp eax, ebx
  jle done
  If the contents of EAX are less than or equal to the contents of EBX, jump to the label done. Otherwise, continue to the next instruction.

## Slide 30: Comparison
cmp — Compare
Compare the values of the two specified operands, setting the condition codes in the machine status word appropriately. This instruction is equivalent to the sub instruction, except the result of the subtraction is discarded instead of replacing the first operand.
Syntax
  cmp <reg>,<reg>
  cmp <reg>,<mem>
  cmp <mem>,<reg>
  cmp <reg>,<con>
Example
  cmp DWORD PTR [var], 10
  jeq loop
  If the 4 bytes stored at location var are equal to the 4-byte integer constant 10, jump to the location labeled loop.

## Slide 31: String Operations (details later as needed)
ins, outs
  Input/output a string from/to a port
movs, movsb, movsw, movsd
  Moves data from one string to another
lods, lodsb, lodsw, lodsd
  Loads data into a string (DS:[(E)SI]] to (E)AX)
stos, stosb, stows, stosd
  Store data in a string (DS:[(E)SI]] with (E)AX)
cmps, cmpsb, cmpsw, cmpsd
  Compare strings in memory
scas, scab, scasw, scads
  Comapre a string (scan a string)
repm, repe, repz, repne, repnz
  Repeat string operation until condition met

## Slide 32: Subroutine Call and Return
call, ret — Subroutine call and return
These instructions implement a subroutine call and return. The call instruction first pushes the current code location onto the hardware supported stack in memory (see the push instruction for details), and then performs an unconditional jump to the code location indicated by the label operand. Unlike the simple jump instructions, the call instruction saves the location to return to when the subroutine completes.
The ret instruction implements a subroutine return mechanism. This instruction first pops a code location off the hardware supported in-memory stack (see the pop instruction for details). It then performs an unconditional jump to the retrieved code location.
Syntax
  call <label>
  ret

## Slide 33: Interrupts
int/rti— generate and return from a software interrupt
The int instruction generates a software interrupt, transferring control to an interrupt handler. RTI returns from interrupt
Syntax
  int <con>
  rti <con>
Example
  int 3H // debugger breakpoint
  int 80H // linux system call
  rti

## Slide 34
Please attribute Dr. Jim Alves-Foss and Dr. Jia Song, University of Idaho
Except where otherwise noted, this work is licensed under https://creativecommons.org/licenses/by-nc-sa/4.0/ Not withstanding the non-commercial license terms, non-profit educational institutions are granted a non-exclusive license to adapt and use this material, with attribution. Creative Commons and the double C in a circle are registered trademarks of Creative commons in the United States and other countries. Third party marks and brands are the property of their respective holders.
Project sponsored by the National Security Agency under grant Number H98230-17-1-0199. The United States Government is authorized to reproduce and distribute reprints notwithstanding any copyright notation herein.