## Slide 1: Module 0: Introduction
Lesson: Data Representation

## Slide 2: Learning Outcomes
Upon completion of this lesson, students will be able to
  Describe binary and hex data representations
  Describe difference between big-endian and little-endian data formats
  Convert between hex, decimal and binary
  Describe creation of higher level data representations
  Describe Integer, Unsigned integer, ASCII and Floating point data representations

## Slide 3: Digital Data
Digital computer technology is based on binary values: 0’s and 1’s (called bits)
Microprocessors and hardware manipulate individual bits, or collection of bits.
  Bits are often collected together into bytes (8 bits)
  Devices will have a “natural” data size that can be manipulated in a single operation, these are called words, and is implementation dependent. Typical word sizes are 64 bits, 32 bits and 16 bits.
    For a microprocessor, the word size is usually the amount of information stored in the general purpose registers.

## Slide 4: Bits is Bits
Computer hardware provides limited operations on the data values (bits/bytes/words) in the system.
  Copying or moving data, mathematical or logical operations.
These values can be used to represent many different things.
  Memory addresses, integer data, floating point data
  Colors on the graphical display, audio sounds, text
  Status of hardware devices, control signals.
Software can take this even further, combining these 1’s and zero’s to represent anything the programmer wants
  Health status in a video game, Electrocardiogram readings, text messages, movies, names and addresses, payroll data, etc.
It is important to understand how the 1’s and 0’s are being used, and what they are meant to represent.

## Slide 5: Binary numbers
We can write a binary number as a string of 1’s and 0’s such as:
  01001000 or 01101001
  These can be interpreted to represent the numbers 72, or 105 – or the ASCII characters ‘H’ and ‘i’ or colors in a 8-bit true color system. Or any other way the programmer or computer systems chooses.

## Slide 6: Integers
Binary numbers can be interpreted as integers, either unsigned or signed.
For unsigned, each bit represents a place holder for a power of 2.
b7b6b5b4b3b2b1b0 is interpreted as
b7×27+b6×26+b5×25+b4×24+b3×23+b2×22+b1×21+b0×20
Therefore, 01001000 =
0×27+1×26+0×25+0×24+1×23+0×22+0×21+0×20 =
0×128+1×64+0×32+0×16+1×8+0×4+0×2+0×1 =
1×64 + 1×8 = 72

## Slide 7: Integer precision
Precision
  With 8 bits, we can represent 256 unique values 0 - 255.
  With 16 bits, that increases to 65536 values.
  This limits the range (or precision) of values that we can use.
  If we perform a mathematical operation that generates a result outside of the range, then we get an overflow (value too big) or underflow (value too small).
  In an 8-bit system 250 + 10 will not be 260, but rather will be 4 (260 modulo 256), in binary:
    11111010 + 1010 = 100000100
    But this has an extra bit on the left (28 = 256), this overflow bit is usually discarded. Many programming languages will not generate an error if this happens.

## Slide 8: Signed integers
Signed integers are more complicated.
Signed Bit
  One way of representing a signed integer is to reserve one bit to represent the sign. Usually 0 is positive, 1 is negative. The sign bit replaces the most significant bit.
Two’s complement
  Most common way to represent negative numbers
  For example, -28 is created by taking positive 28 (in binary), flipping all bits (0->1 and 1->0) and adding one.
    00011100 -> 11100011 -> 11100100

## Slide 9: Signed integers (continued)
Two’s complement
  Notice that the left most bit is a 1. This will always be true of a twos complement representation of a negative number
  Used for efficiency
    Computers can use the same hardware to add and subtract unsigned and 2’s complement signed integers. The hardware does not even need to know if the number is positive or negative.
  Range of numbers for n bits is -2n-1 – 2n-1 - 1
Number of Bits | Minimum Number | Maximum Number
8 | - 128 | 127
16 | - 32,768 | - 32,767
32 | - 2,147,483,648 | 2,147,483,647
64 | - 9,223,372,036,854,775,808 | 9,223,372,036,854,775,807

## Slide 10: Hexadecimal representation
Instead of writing 1’s and 0’s it is easier to write a binary value in a more compressed notation.
  Since binary numbers can be mapped to powers of two, we can write every 4 bits as a base 16, (Hexadecimal) number.
  The hex digits are 0,1,2,3,4,5,6,7,8,9,A,B,C,D,E,F
  A represents 10, B is 11 up to F which is 15.
  Now our binary number 01001100 can be written as two hex digits: 4C . To differentiate this from decimal, we usually precede the hex number with ‘0x’ as in ‘0x4c’
  This value is 4 x 161 + C x 160 = 4 x 16 + 12 = 64 + 12 = 80

## Slide 11: Endianness
We have been writing our numbers with the most significant digit (the largest value) to the left. This is how we write decimal numbers.
  2614 – the most significant digit is the 2 in the “thousands” place and the least significant is 4, in the “ones” place.
  On paper, and in text and code, we will always write our numbers this way. In a computer system, values may be stored differently in memory.
    A 32-bit integer takes four bytes in memory, stored in 4 consecutive memory addresses.
    If the least significant byte is stored in the lowest memory address, we say the system uses little-endian byte order (Intel processors)
    If the most significant byte is stored in the lowest memory address, we say the system uses big-endian byte order (Power PC, SPARC)
    ARM processors allow you to choose endianness.
    The default network byte order is big-endian – most significant byte is sent first. Therefore little-endian (Intel) processors have to convert network-based integers.

## Slide 12: Credits
Please attribute Dr. Jim Alves-Foss and Dr. Jia Song, University of Idaho
Except where otherwise noted, this work is licensed under https://creativecommons.org/licenses/by-nc-sa/4.0/ Not withstanding the non-commercial license terms, non-profit educational institutions are granted a non-exclusive license to adapt and use this material, with attribution. Creative Commons and the double C in a circle are registered trademarks of Creative commons in the United States and other countries. Third party marks and brands are the property of their respective holders.